Demystifying ICC
Scaling and incorporating enclaves in embedded systems.

---
What and why embedded ICC
- ICC – Inter Core Communication; the act of control and transferring data from one core to another.
- This can be between separate microcontroller chips using a serial or parallel signalling protocol, between separate and independent cores on a single piece of silicon using a purpose designed peripheral or between cores in a tightly integrated processor fully sharing memory as in a conventional multi-core processor.
- Involves inter-core interrupts, data messaging, buffering, shared atomic operations, shared synchronisation primitives and controlling RAM/executable access.
- But why have more than one core?
  - Reduce power usage - two cores running at half the speed uses less power than a high speed core; e.g PC overclocking massively increases power consumption for a comparatively smaller performance increase.
  - Isolation – A core running certified code with restricted access to and from the rest of the system can greatly simplify security and compliance concerns.

---
Illustrative multi-core architectures
Each core now has an independent RAM data cache, the contents of RAM is now incoherent.
Much higher data bandwidth can now be consumed by each core.
The firmware must co-ordinate cache write-backs and have a clear system of RAM ownership to avoid data races.
Use data guards and keep each RAM cache line only ever written by a single core at a time separated by co-ordinated transfer of ownership to another core.
Each core only has an instruction cache; all data reads and writes go to RAM and so are coherent between cores.
The flash has a read ahead flash for better latency and bandwidth.
Flash controller can only write when flash reads are disabled; the cache can still serve data but needs stale data evicting.
Put the vector table and firmware bus error handler in RAM to wait for flash and then resume exec.
Use shared flash write vetoes for time-sensitive operations.
Keep an independent data caches per core to maximise core data bandwidth, but have caches automatically trigger a write back in another cores cache before fetching that cache line.
A H/W optimisation is to pick up the cache line contents as the other core writes it to RAM.
Avoids any cache line being present in more that one cache therefore the caches are coherent.
Always slightly fetching cache line.
Bouncing cache lines between cores causes slowdowns.
Use a unified multi-port cache to increase the data bandwidth compared to all cores using the same data bus and share cache lines coherently between cores.
Much simpler for the firmware to operate correctly an the performance penalty for writing to the same cache line is small.
High silicon cost with increasing number of cores so there is an upper economic limit on the number of cores.
Cross $ WB triggers
Peripherals incl
flash controller
Peripherals incl
flash controller
Flash
Flash
Shared I & D port
Shared I & D port
RAM
RAM
Core
I $
Core
I $
Core
I $
Flash
Peripherals incl
flash controller
RAM
Shared I & D port
Read ahead I $
Read ahead I $
Flash
Peripherals incl
flash controller
RAM
RAM
D $
I $
Core
RAM
D $
I $
Core
RAM
D $
I $
Core
Shared I & D port
Core
I $
Core
I $
Core
I $
Read ahead I $
Multi-port $
Read ahead I $
RAM
D $
I $
Core
RAM
D $
I $
Core

---
ICC mechanisms
- Interrupt lines between cores – requesting attention or signalling an ICC state has been updated.
- Addressable state via a data bus – allows limited specific communication of pre-determined meanings.
- Communication peripheral – a serial/parallel peripheral acting as a transport mechanism for data messages to a secure memory copy mechanism.
- Shared memory accessible by both cores to pass data messages between them.
- Most of these mechanisms can be used between cores on the same piece of silicon and between cores on different pieces of silicon/chips.
- Higher level structures, conventions and patterns are built on these mechanisms including those used by an OS.

---
Example shared memory ICC
NB: These apply to both inline messages and pointers to messages.
RAM cache lines
Notice board for simple atomic data. One writer => Many readers.
H/W ensures atomicity of individual 4/8 byte values published.
Notice board for compound data using top & bottom generational version guards and optionally multiple buffering. One writer => many readers. Increment top, write data, increment bottom to write. Read by pre-check guards, copy entire range and then re-check, retrying as needed.
Cache line batched circular buffer with ownership of each block (1+ cache lines) indicated within a header. One requester, multiple responders. Each request has a nominated responder; all responders must iterate though available messages to find their ones.
Sender position for oldest response not processed.
Sender position for next request; once prepared, ownership is transferred to the responder.
Green’s responder position for processing next.
Cache line batched circular buffer with mutex write protection. Multiple requester, multiple responders. Each request has a nominated requester and responder; both responders and requesters must iterate through available messages to find theirs.
Mutex protected next entry position which is unowned.
Blue’s oldest message search position with an available response.
Red’s oldest message search position waiting for a response.
Purple’s oldest message search position with an available request.

---
ICC patterns
- ICC patterns include all the typical concurrent data patterns:
  - Shared state synchronisation (settings, control or status updates).
  - Message passing queues.
  - Query and response.
  - Notifications.
- The same difficulties that can be encountered with concurrent systems also impacts ICC and the same techniques can be applied to avoid the common pitfalls of:
  - Deadlocks.
  - Non atomic state updates.
  - Data races leading to erratic timing dependant behaviour.
  - Software and hardware caching and coherency.
- The various ICC mechanisms are more efficient at implementing some specific patterns than others.

---
ICC message patterns
A query / request sent to a recipient that triggers a web of communication.
A single notification message sent to a recipient.
1
2
Initiator
Recipient
Recipient
3
4
5
Sending a query / request to multiple recipients, each of which responds separately.
A query / request sent to a recipient that responds.
Sending a query / request to multiple recipients, the message chain pattern evolving individually for each recipient.
A query / request sent to a recipient that proceeds to form a chain of communication.
Message passing / Single and multiple recipient variations.	Synchronous / Sender blocked until message processing has completed.	Asynchronous / Sender continues execution while message(s) being processed. / Sender uses a token / lookup to determine when message has been processed or a response is available. / Unmodifiable and modifiable pending message variations.
Notification / No response.	Single notification with sender continuing execution after the notification has been processed.	A queue / table of notifications pending processing by recipient(s).
Query / Request / Response required. / A chain of 2 or more messages per recipient.	Single outgoing message with sender blocking until all messages of a chain has been processed. / For multiple recipients either use a callback for the response or iterate over the responses as they arrive.	A queue / table of messages pending processing by recipient(s).
Initiator
Recipient
1
Initiator
Recipient
1
2
Initiator
Recipient
1
2
3
Initiator
Recipient
1
3
Recipient
1
2
Initiator
Recipient
1
3
Recipient
1
2
4

---
ICC data messages options
- Serialise the message data through a peripheral using interrupts to alert the receiving core which must progressively decode the message to determine when it has been completely received.
  - Slowest due to the data copy into and out of the peripheral and the need for progressive decoding by the receiver to identify if a complete message has been passed but has the greatest isolation between the cores.
- Copy the entire message into a shared memory message buffer, set the buffer status and alert the receiving core via an interrupt.
  - Only requires a single copy of the message data into the shared message buffer with the buffer status avoiding the need for partial decoding.
- Fully share memory between the cores and send the address of the data message into a buffer and alert the receiving core using an interrupt.
  - Fastest by avoiding any copying and allows the use of compound data structures but requires that the sending core leaves the message data unchanged until the receiving core has finished with the message.

---
Passing memory ownership
- A variety of possibilities:
  - Memory ownership explicitly returned to the allocating core via the API design, e.g. REQ_resource → AVL_resource → REL_resource API pattern. This is the most flexible and most obvious to use but is vulnerable to special case bugs.
  - Have a dedicated batched memory return (optionally with on request purge), e.g REQ_resource1 → AVL_resource1, REQ_resource2 → AVL_resource2, AVL_released_resources. This is potentially more efficient as it sometimes avoids an extra message in your API but does add complexity into buffering up and optionally requesting available memory back.
  - Have a global memory allocation system; a lightweight version of those used on multi-thread/core computers so that a different core can free memory than the one that allocated it. This can be rather challenging to implement and consume a significant amount of CPU time as well as program space but it minimises the amount of message passing as well as avoiding the need for specific API construction or special handling of the memory.
- If data is being passed across a trust or isolation barrier, be very cautious of accepting memory buffers or sharing memory as this degrades the safety and isolation and requires special handling.

---
Asymmetric Multi-Processing AMP
- Every core runs an independent OS where all tasks remained pinned to a single core.
- The application code running on each core arranges it’s own communication and division of effort between cores, requiring greater care in the design.
- A far simpler OS design can be used such as vanilla FreeRTOS rather than the cost associated with an SMP OS (specialised hardware and/or implementation speed).
- Depending on the hardware, the cores can be heavily isolated so that they cannot effect each other except via highly restrictive mechanisms or in the opposite extreme memory can be fully shared shared and exchanged between cores (requires care to return allocated memory back to its originating memory pool).
- Isolation between cores and activities can be highly beneficial for some applications, especially for security and certification concerns.

---
Symmetric Multi-Processing SMP
- An SMP system has an OS that is able to schedule tasks across multiple cores to utilise any available processing resource.
- ESP-IDF is an example of a FreeRTOS implementation ported onto a multicore ESP32 microprocessor with SMP operation.
- Generally simpler to create code that can utilise the cores effectively but has potential inefficiencies with cache coherency and synchronisation / atomic primitives.
- With a single core OS it is relatively simple to implement synchronisation and ensure atomic operation. e.g. FreeRTOS uses taskExxx_CRITICAL() to disable/re-enable OS relevant interrupts so that memory and data structures can be atomically modified and synchronisation primitives easily provided.
- SMP systems need synchronisation and atomic operations that span all the cores in the system without imposing excessive overheads; the operation of all cores must be co-ordinated.

---
SMP atomics and synchronisation
- The operations that need atomics and synchronisation include:
  - Memory allocation and release.
  - Modifying task state structures.
  - Appending and removing items from queues.
  - Read-Modify-Write and Read-Copy-Update operations.
  - Mutexes, semaphores, mailboxes, forking and joining threads.
- Example - providing a mutex involves:
  - Atomically and uniquely identifying the thread that holds the mutex even if multiple threads running on different cores simultaneously attempt to take it.
  - An atomic count of the number of times the mutex is held even if the thread that holds the mutex swaps between cores and any cache coherency problems must be resolved.
  - Having all threads that fail to take the mutex be able to add themselves onto a wait list so the OS can efficiently identify and wake threads waiting on the mutex in a fair way when the holder has released it.

---
SMP atomics and synchronisation
- Some hardware provides direct support for implementing these
  - x86 cmpxchg instruction: If the memory address contains an expected value then change it to a new value, returning the previous value and if the exchange happened in status flags. This can be executed atomically across all cores to provide a simple spin lock or the foundation of a semaphore / mutex.
  - Multi-core microcontrollers may have been designed to globally disable some interrupts and have a global lock peripheral. The disabling of interrupts prevents an interrupt from entering and having to spin. The global lock would only be held while updating a particular semaphore / mutex state to claim or release it.
- There are software algorithms to select a global lock holder but they can be slow and have significant difficulty with both interrupts and incoherent caches.
  - Peterson’s or filter algorithm for two or more threads.
  - Require that all memory accesses are not pipelined, propagate immediately between all cores and the memory contents is not cached.
  - Vulnerable to priority inversion problems.

---
Hybrids of SMP & AMP
- On a system with ≥3 cores, they could be utilised in a hybrid of SMP and AMP where ≥1 cores have an AMP OS running on them while ≥2 cores are running an SMP OS.
- The motivation to do this is to incorporate the relative merits of both approaches into a single device.
- The SMP cores makes it easier to utilise the computational performance of the multiple cores with automatic load balancing and efficient data passing utilising the shared memory that is required for SMP operation.
- The AMP core(s) allow much more predictable core loading, memory usage and timing and can be utilised for specialised operation. If memory isolation is in place for the AMP core(s) then this assists with many security and certification goals.
- One possible security feature of an AMP core is providing security enclaves that provide certified functionality in a secure manner.

---
Enclaves and sandboxes
- Recent Intel x86 processors have implemented Software Guard Extensions (SGX) to execute code that must be run at a higher level of security and trust compared to the calling code and OS/hypervisor by keeping all executing code and working memory used encrypted.
- Whilst SGX has some attacks demonstrated, it is clearly desirable for security conscious features despite the silicon and performance cost.
- A far simpler and practical approach for embedded systems is to use an AMP core with hardware memory protections and certified hosting sandbox firmware; sandboxed product specific behaviour then does not impact the certified security enclaves.
- Input and output data can be passed into and out of the enclave using any of the ICC mechanisms and patterns used in any other situation.
- Consideration should be made to utilising the more restrictive ICC mechanisms to ensure isolation.

---
Sandbox hosting
- Enclaves can be executed along-side insecure application code by running then in isolated sandboxes, controlling access to peripherals and supporting a hypervisor style interrupt system which automatically switches the current protection domain.
- This requires non-typical hardware support and care must be taken with data interfaces; a single certified robust mechanism is ideal but limiting. Specific time-windowed access to untrusted memory generally allows higher performance in data processing tasks.
- Certification is much easier if all certified and manufacturers code is run on separate cores from 3rd party application code as this reduces the potentially accessible surface area to be attacked.
- Include mitigations to software exploits and hardware attacks such as debug probes, power & clock glitching, physical data injection or external data forging by including a variety of overlapping measures and minimise the amount of internal information that can be potentially exploited.

---
Example crypto enclave
AXI bus
- The purpose of the crypto enclave is to perform batched H/W assisted crypto operations using securely held keys.
- Example four core SoC with per core H/W address based access protection with H/W crypto.
- The sandbox layer runs on all cores and enforces isolated executable image, data FLASH and data RAM with integrity checking.
- The crypto enclave is restricted to a trusted core, although the enclave itself does not have full trust.
- Can access less trusted RAM and FLASH to perform requested crypto.
Flash controller
Flash
Shared I & D port
RAM
I Read ahead
D & I $
RAM
D $
I $
Core
AC
DMA
RAM
D $
I $
Core
AC
RAM
D $
I $
Core
AC
RAM
D $
I $
Core
AC