12 steps to firmware packages

---
So what is this all about?
- How to securely design chips and firmware for integration into 3rd party products and distribute firmware securely for use during manufacture, 3rd party development process and distribution to installation engineers or end users.
- All of these techniques are industry standard but not used enough by cost conscious manufacturers due to the lack of expertise.
- I want the devices I buy for myself to be more secure!
- Always involve a security auditor during product development:
  - To review your architecture.
  - To review your prototype code.
  - To audit your production implementation.
  - To audit your source repository security measures.
  - To audit your manufacturing and data storage tooling and processes.
- No there aren’t aren’t really 12 steps; identifying the correct reference is left as an exercise to the reader.

---
System components
Manufactured chips database with their private keys
Least vulnerable
Firmware packaging
Firmware repository
Most vulnerable
Firmware distribution portal
Custom microcontroller
ROM
RAM
FLASH
SECURE DATA
CPU
TEST & DEBUG
Debug probe and test equipment
In use by 3rd party developers
In use by own developers
In use during manufacturing
Programming / update tools
In use by own developers
In use by own developers
In use by 3rd party developers and end users
Source code and build servers
Accessed by own developers
Accessed by 3rd party developers and end users

---
Silicon mitigations
- CPU isn’t that vulnerable
  - Generally isn’t significant which CPU you use.
  - Very little data is stored in the CPU itself.
  - Allow the synthesiser to scatter the CPU around the digital section of the chip to obfuscate its internals.
  - Split registers and buses make it hard to inject values / read them out and shadow their metal layer connections so it is hard to simultaneously access them.
  - Keep the buses and register connections on lower metal layers.
- Split X means:
  - Duplicate the functionality into A and B parts and obfuscated by a value that is randomised at boot and can be regularly scrambled by SW.
  - The true value being stored / passed is F(A, B, Val) .
  - Has a non-trivial silicon and complexity cost.

---
Silicon mitigations
- All secrets should be put in a secure data hardware block.
  - This is a deliberately obfuscated RAM and FLASH like peripheral that has been specifically hardened against attack:
    - Silicon has been pre-designed to be hard to probe.
    - Uses built in corruption detection.
    - May have a suicide function that will prevent further use, erase stored data and even damage itself if it is being misused / probed.
    - Has an obfuscated address space so an attacker must reverse engineer the software to be able to read out the contained data.
    - May have a H/W encryption engine to avoid exposing a key.
  - Comparatively expensive, slow with limited capacity but a much more secure place to store a small amount of key material.
  - Ultimately the contents can be read out / used (as the device has them there because they are needed by the device)
    - Do not use the same key for every device!
    - Ideally each device would have a unique set of keys.

---
Silicon mitigations
- RAM and FLASH are easily identifiable and generally quite practical to read out in their entirety.
- Mitigation is difficult:
  - Could split their entire contents but that doubles the silicon area.
  - There always needs to be an unencrypted region to execute from which will contain the means to access the rest.
  - Attacker can change the contents if they need to.
- An encryption and scramble system for your non-working data in the RAM and FLASH will obfuscate their contents and prevent leaking of old data space.
- If you’ve got a scrambled bus CPU then that slows down an attacker by requiring them to use the CPU and secure data peripheral to access the data rather than just reading it out.

---
Silicon mitigations
- ROM can be mitigated in a couple of ways:
  - Hidden in the synthesised digits to make it unidentifiable.
  - Use a specific metal interconnect layer in a well defined region which looks the same irrespective of content so an attacker would have to read it out (or etch down the metal layers) and change any public key for every mask set.
- Never put any secrets in ROM; they will be exposed.
- Hard for an attacker to change to gain execution control of the CPU.
- Much cheaper than RAM or FLASH so split and scramble is more practical if your CPU supports it.
  - It has to be identical for every device made from a given mask set so this only hinders the initial attack and doesn’t protect other devices since the contents are usually the same.

---
Silicon mitigations
- Test and debug support needs to be irreversibly disabled to stop an attacker from using them to access the chip.
  - Multiple positions in the logic elements and data paths need to be severed to prevent an attacker driving the silicon using probes.
  - Causing physical damage by burning out multiple silicon areas tends to be fairly irreversible.
- An access code to re-enable debug is popular as it allows an authorised developer / tool to gain access but this is harder to secure from an attacker probing the silicon to enable debug.
- Having multiple mechanisms to disable debug (e.g. both a hardware and software enable / disable control) operation and access to the buses adds additional hurdles for an attacker.

---
Tooling
- Chip test and initial programming during silicon manufacturing.
  - Device is most vulnerable now when it only has it’s ROM.
  - Somewhat protected by the ROM shared asymmetric key used to validate the initial image.
  - Unchanging nature of a ROM key means that an attacker can attempt differential analysis if they have access to multiple versions of the initial image.
- Debugger for use by developers gives a great deal of internal access to the chip
  - Could be used to extract or deduce key material by an attacker.
- Device updater (only needed if the device does not have built in connectivity).
  - Provides raw connectivity; the device-server connectivity and data is all encrypted but it gives an attacker an opportunity to look for connection and encryption flaws.

---
Initial chain of trust
ROM public key
- Physical device tied:
  - Per mask set master shared asymmetric key in ROM to authenticate first software image at boot time.
- Randomly generated by ROM using chip testing entropy:
  - Per device master private symmetric keys to encrypt internal data.
- Added as the final step of chip testing:
  - Per batch shared asymmetric key in secure data element to authenticate subsequent software images and respond to challenges.
  - Per device private asymmetric key in secure data element to issue challenges.
  - Initial image.
Test and programming equipment
Secure servers
Request to permanently switch out of manufacturing test mode and start initial programming process
Per device generated public key and challenge code
Server challenge response using diffie-hellman derived shared secret and initial firmware image signed by server
Per device settings and security assets encrypted using shared secret.

---
Maintaining the chain of trust
OR
- There are multiple reasons for non-developers to legitimately gain elevated access to the device: installers, repairs and updates (for devices without built-in connectivity).
- Require all tools to be internet connected and simply pass encrypted data between the device and your server which will provide summary information back to the user.
- Ratchet the communication encryption key at least once per session.
  - Device flash write endurance prevents continual ratcheting.
  - Consider ratcheting every 15 minutes or so during a session.
Secure servers
PC
Relay
User summary
Public device ID and encrypted challenge code
Challenge response and ratchet initiation.
Ratchet confirmation and device status
Batched operation instructions and information

---
Manufacturing and developer access
Relay
- During manufacturing and development it would be less secure and very slow to route all communication via servers.
  - The manufacturing device / developer has access to the raw data being sent; encrypting it is just assisting an attacker in breaking the communication encryption.
- The secure unlock process gives the server to block any suspicious pattern of unlocks.
- The device itself can restrict its functionality if multiple unlock failures encountered and aggressively limit unlock attempts or even permanently disable itself on multiple challenge failures.
- An unlocked device should periodically issue a new challenge.
Secure servers
PC
Public device ID and encrypted challenge code
Challenge response and ratchet initiation.
Ratchet confirmation and device status
Unencrypted direct control by developer
Command to switch into development mode

---
Software updates
OR
- Secure server can limit the people who can decide if a device should be updated.
- An image is encrypted with its own image specific key so that no delta attacks can be applied to a single image going to multiple devices.
- The image key must be provided in amongst random data to avoid delta attacks utilising the constancy of the encryption key for a given image.
- The image itself should start with and include within it fixed chunks of randomly generated data to hinder sequence probability analysis.
- A whitening function with per image configuration, should be applied to the actual image data so that common / likely patterns are removed (e.g. blocks of zero’s or FF’s).
Secure servers
PC
Relay
User summary
Public device ID and encrypted challenge code
Challenge response and ratchet initiation.
Ratchet confirmation and device status
Image encryption key provided with defensive random data.
New images encrypted with their own key and including defensive masking data and whitening.

---
Crypto safety
- The plaintext needs to be significantly different for each encryption key used to minimise the potential for differential analysis.
  - This is why no per device image encryption / signing should be used as the images would be too similar.
- Make your own test equipment and integrate it into the chip manufacturer test system.
  - Include hardware tamper detection to minimise the risk that the equipment itself has been compromised.
  - Require the test equipment to be manually re-approved on every boot before it can operate or communicate with your servers.
  - Keep all images and keys in the test equipment RAM.
- Each time the device completes a challenge / counter-challenge cycle then those keys should be ratcheted to change them.
- Each image should derive new image signing and encryption keys from the physical and batch master keys.

---
Firmware image protection
- Only applied to released images (not developer debug data as the intact unencrypted binaries was generated and is present on their computers anyway).
- Image data is split into chunks of varying length.
- Chunks are reordered using throw-away cryptographically secure random numbers.
- Random data chunks are inserted (with one always at the start) to make data analysis harder.
- All data is whitened using randomly chosen per image settings to avoid predictable statistical correlations in the data.
- Add a crypto prefix of randomness and derivation information.
- Derived keys from unique securely stored ID’s.
Unecrypted image
1
2
3
4
5
6
7
5
3
7
1
2
4
6
-
5
-
3
7
-
1
2
4
-
6
-
5
-
3
7
-
1
2
4
-
6
-
5
-
3
7
-
1
2
4
-
6
-
5
-
3
7
-
1
2
4
-
6
Encrypted image

---
Layered images
- Over time you will accumulate multiple products to support and update, each with:
  - Different instruction sets => multiple recompilations.
  - Different microprocessors => different chip peripheral code.
  - Multiple pcb’s => pcb specific configuration and adapter code.
  - New bootloader and security measures => must be updatable.
  - Different purposes => application specific code.
- Minimise the number of reproduced images (same/similar data encrypted differently multiple times) by separating out these concerns into separate encrypted images, reducing the potential for a differential attack on the encryption keys.
- This can also minimise the cost of porting and supporting a wide range of hardware at the cost of requiring global changes to change an interface.
- The encryption implications of changing ISA’s is not obvious.

---
What is a firmware package
- This is a collection of all the materials relating to a device and is designed to be cached by tools to save the bandwidth of repeated downloading.
- Contains the unencrypted necessary information to allow tools to communicate with and interpret diagnostic information coming from the device.
  - This is included in the firmware package so that developer / diagnostic tools can work with a device without requiring a specific version of each tool for a given device.
- Includes the encrypted images sent for a device update which includes:
  - The firmware image(s).
  - Configuration blobs for a given 3rd party product.
  - Configuration blobs for a given product revision.
  - Configuration blobs for a given user.
- Does not contain any decryption or signing keys.
Firmware package ID
Details of how to communicate and interpret data from the device once the challenge / counter – challenge is completed.
Session encrypted between tools and server.
Human readable details
Signed and encrypted firmware image
Signed and encrypted configuration blob

---
Firmware package use in debugging
- Contains a simple statement of the connection method (but no keys) for this firmware and how to request information from the firmware.
    - Different firmware releases can behave differently so the firmware package contains the needed information rather than have different tools for different firmware versions.
- Contains a prescription on how to decode the binary debug messages and events that can be produced by the device when enabled.
- Contains device information so that the debugging tool can accurately display the device status based on the debug information.
    - Flash utilisation and fragmentation.
    - Memory utilisation and fragmentation.
    - Chip peripheral operation display configuration.
    - Device state machine interpretation and message sequence chart labels.
    - Automatic deduction of derived values from debug information that have been useful to developers in the past.

---
Server data stored
- Device
    - ID
    - Product type
    - Last known firmware
    - Recommended firmware
    - Private ROM asymmetric key
    - Per batch private asymmetric key with ratchet status
    - Per device shared asymmetric key with ratchet status
    - Device connection history for malicious behaviour detection
- Tool
    - Tool software and version
    - Authorised users
    - Per install shared asymmetric key with ratchet status
    - Manual authorisation history
    - Usage history for malicious behaviour detection