Bandwidth limited logging
Tiny embedded systems to servers

---
Logging systems I have created
- For 256 byte RAM microprocessors to 32GB RAM servers.
- Used in space, on aircraft, in servers, by developers and end users.
- Different techniques are appropriate for different devices and situations; using / maintaining an in-house library of techniques is recommended which you can then use pick and mix style.
- Not programming language specific; they have been used with C, C# & golang.
- Primary design goals:
  - Minimum disruption to the execution timing.
  - Dynamic configurability.
  - Bandwidth efficiency.
  - Support for extreme logging verbosity.
  - Compactness of invocation in source code.
  - Low maintenance and ongoing development effort.

---
Logging architecture superset
- Some example implementations that use a subset of these will be shown later.
- Modes of potentially simultaneous operation:
  - Saving logs persistently.
  - Streaming logs out to a log aggregator.
  - Directly observing generated logs.
  - Searching for and downloading logs.
  - Pre-programmed logging conditions (e.g. keep last <=25MB & <=5s of debug logs in RAM and stream them out + add to persistent local storage if an error occurs).
- A log aggregator receives log streams from other devices but otherwise is the same.
Deferred execution
of logging
Log filtering
Prioritised RAM
buffer with eviction
Prioritised bulk
buffer with eviction
Prioritised bandwidth
limited streaming
Log search
and matching
Interactive debugging
Settings configuration
Logging statement
or log receiver

---
Example: Sensor interface
- Small microcontroller for controlling and monitoringa sensor via a data bus as part of some unattended equipment.
- Requirements:
  - Minimum power consumption.
  - Very low telemetry bandwidth with occasional connectivity.
  - Report recent events on error only.
- Must store normal data for long periods until the RF system is available; an error will trigger one or until a scheduled RF session.
- Cyclic buffer of normal events that is frozen upon first error so background data is provided with the error report.
- Memory efficiency of log entries is paramount so they are designed to be of minimal size in memory and expended into full data bus packets on transmission.
- Sensor reports created when needed for an RF session (not shown).
Prioritised RAM
buffer with eviction
Send after error only
Logging statement

---
Example: PC application
- Application running on users computer.
- Requirements:
  - Ease of providing support to users who are not sure how to use the application or what the appropriate settings to use are.
  - Maintaining responsiveness while logging.
  - User privacy.
- Only sends error reports with user permission which are assembled from the logs.
Interactive debugging used during development and when providing support; manual authentication on establishing a debug connection by the user is needed to prevent invisible malware exploitation.
Deferred execution
of logging
Log filtering
Prioritised bulk
buffer with eviction
Sending of error
Reports to server
Interactive debugging
Settings configuration
Logging statement

---
Example: Server component
- Single instance of one component from a replicated server system.
- RAM holds recent logs down to trace level detail so that they can be examined by remote debugging / sent as error run-up logs.
- Local storage is not arbitrarily large or fast so only keep info/warn/error logs for a finite time.
- All local storage and RAM can be searched / downloaded remotely as required.
- Log aggregation servers are used, but the machines themselves, data storage and bandwidth are not free.
Only summary and processing information that are expected to be of use plus a full replay of trace level logs in the run up to an error get sent to the aggregator.
Deferred execution
of logging
Log filtering
Trace level RAM
buffer with eviction
Prioritised bulk detail
buffer with eviction
Prioritised bandwidth
limited streaming
Log search
and matching
Remote debugging
Settings configuration
Logging statement

---
Logging as archiving
- In addition to recording logs, there are a variety of other reasons for recording data for some products:
  - Business: there is some value to the data that must be retained, e.g. tracking virtual currency use.
  - Contractual: e.g. there is a clause to record operational data.
  - Legal: e.g. some data must be retained by law.
- These could be satisfied with their own log like systems which would make a very clear distinction between discardable log statements and essential to be retained unmodified records.
- Using the same system reduces the amount of development work and hopefully gives your logging the reliability and testing of the more highly regarded record keeping.
- If the same system is to be used for both, ensure that the generation and retention of the records is fixed at compile time and preferably use a different recording statement to emphasise their importance.

---
Logging statement 1
- Never forget the basics; always support a simple printf log statement.
- Design choice: where should the logging cost fall?
  - In the logging context? => Potentially the most efficient but also the largest impact on responsiveness.
    - e.g. Log(Debug, ”Buffer status: {buffer.Count}/{buffer.Capacity}”);
    - The entire log statement is being prepared with the cost for this occurring during execution.
    - Has a constant overhead so minimal timing changes but the cost is always incurred.
    - No concurrency issues; the resultant string is not mutable or dependant on mutable local data.
  - Dispatched to a logging context? => Potentially lower impact on responsiveness but there are there are now concurrency concerns with the data being used for making the log.
    - e.g. Log(Debug, BufferStatusLogMsg, buffer.Count, buffer.Capacity);
    - The construction of the log statement is being deferred (in the case of the windows performance metrics, it is deferred right until the logs are viewed).
    - Need to consider concurrency issues; any data logged must either be immutable or copied.
    - The out of context processing can be moved in context via a run time configuration.

---
Logging statement 2
- Design choice: should the overhead change with log settings?
  - Only use context CPU time when needed => Minimum processor cost but the greatest timing differences when logging is enabled.
    - The log statement itself evaluates if this log is currently enabled and returns if not.
    - You cannot get pre-event (on error / trigger condition) background information with this choice; the information was simply never captured.
  - The logging context CPU usage remains the same but logging background threads only consumes CPU when needed => Higher context CPU usage with slower system operation but all information recorded.
    - A log statement always stores all log data into RAM, relying on the buffer eviction to weed out the unwanted logs.
    - Usually, but not always, avoids the occasional mysterious log level dependant bug that goes away when logging is turned up but still changes system resource usage, particularly storage.
  - Keep CPU, disk and network usage as constant as possible => Minimum possibility for service disruption when logging is configured at the highest cost.
    - Done by overwriting dump files and marking network reports as for discarding.
    - Very limited situations where this is desirable or needed.
- This can be configured at run time as circumstances change.

---
Logging statement 3
- Design choice: identification of the log messages?
  - Explicit by the programmer => Most likely to have errors, especially after refactoring, and can be tedious for the programmer.
    - Unless strings are used as identifiers then this merges quite poorly.
    - Language id features like __FILE__ macros and file scope logger objects help.
  - Runtime cached reflection based identification can scan through your code, producing an enumeration and translation automatically if you are using a suitable language (e.g. C#) and can afford the code size & start-up time cost.
    - Code obfuscation directly works against this, but some functionality can be retained.
  - Use a language pre-processor as part of your build process to perform an enumeration and construction of translation files at compile time.
    - Requires a usable language parser and code injector for your language, providing a lot of flexibility at the cost of an complex implementation which needs careful consideration.
    - Potentially has the minimum runtime size and resource usage for a given logging requirement.
    - As this is a ‘compiled’ logging system, the implementation can be swapped out and customised for the circumstances allowing the production system to be different from the under development or under test system with different levels of integration into other infrastructure.

---
Log definitions
- There are several ways to consider log data:
  - Simple human readable text that is not primarily machine parsable.
    - A simple text log like many applications produce.
    - Can be parsed but at the cost of execution speed and developer maintenance.
  - Data structures with a fixed layout and no dynamic length data (except optionally the final element of the message).
    - Simple binary blob with fixed data field positions, lengths and byte ordering.
    - For appropriate programming languages this permits extremely fast memcpy’s from structs for compile time specified logs which is desirable for embedded logging systems.
  - Data structures with dynamic length or optional elements that utilise other fields to determine their length / presence.
    - A log representation that maps directly to the representations possible for most programming languages.
    - Needs encode/decode routines to deal with the variability.
  - An arbitrary encoding system where successive encode/decode steps are determined by a decision tree for each step of the process.
    - The most generic possible system that can be extended to encompass any data format.
    - Usually processes run-time data specification and is the most complex and slowest.

---
Log data 1
- Design choice: is every log statement unique and independent?
  - Do log statements have common and identified data structures?
    - Doing so usually reduces the number of encode / decode routines needed.
    - There is an increased potential for accidentally causing inadvertent log changes elsewhere.
    - Minimising the number of data structures usually increases the average size of logs due to optional/situationally valid quantities.
    - Allowing a single log statement to use multiple different data representations depending on the data values being logged increases the number of data structures.
  - Is the log level an intrinsic part of the log statement?
    - If it is then the log level is encoded simply in the presence of that log statement; having it explicitly identified is a convenience rather than a necessity => this could be customised at run time if desired rather than always hard coded depending on the situation.
    - If it isn’t then the log statement could have a level that changes according to the data it holds => is it then desirable to be able to change the limits at run time that would elevate a log level from trace to debug or from info to warning?
  - How are quantities in the logs to be identifier to the user?
    - Is each field in every log a different quantity? (e.g. is periodic_summary_log.allocated_mem a different quantity from high_memory_ressure_log.allocated_mem and should not be shown together?)
    - Is every identical field name a single quantity and so can be search for and displayed together?

---
Log data 2
- Design choice: how to generate the individual log specific code?
  - Manually by developer in every language => time consuming, error prone and a nightmare to change between software versions.
    - There is just too much to do for anything other than small scale software.
  - Using a multi-language serialisation/deserialisation library or code generator => great time saver but still requires manual implementation of data capture and data interpretation & display.
    - There are some very popular and capable multi-language libraries and code generators like protobuf.
    - Text serialisation such as XML, JSON or YAML will be significantly larger and much more CPU intensive than a binary format.
      - Being fairly self describing does allow the use of general purpose data handling, search and display libraries, much like the ‘big data’ hype.
      - Compression of individual text log entries is usually of limited effectiveness unless it is very large or being used across a stream of log entries.
  - Building / reusing some dedicated logging infrastructure => domain specific code generators have the greatest automation but have the highest complexity and time cost to understand, maintain, debug and implement.
    - General purpose log handling is based on a ‘master’ description of the logs from which target log statements, encode/decode and log search / viewing is based.

---
General purpose log handling
- After having to do some / most / all of it manually one or two times you will definitely find that this is the most efficient overall approach by far and becomes a high level selling point to customers.
- Design a log definition system such that the correct definition can be easily identified and obtained automatically.
  - Debug logs should always include regular identification information to do this.
  - Need to be able to automatically obtain the definitions for each firmware build; have a step in your build system to automatically upload them to a suitable server.
- This requires that all tools and software use run-time based definitions of the debug log data (other than potentially the software doing the logging) including:
  - Decoder plug-ins to provide compiled decoder, analysis and display add-ons.
  - Run-time definition of the data allowing general purpose logic to use the logs.
  - Have a conversion program as a preprocessing step or service to convert the logs into a generic machine readable format (using either of the two previous approaches).

---
Build time generation of logging statements
- The concept is to mark data structure fields (in a language specific way or simply with comments) as to the quantity being held in a data structure field.
  - A pre-build code parser can then identify all these debug relevant quantities and construct any necessary code to extract these quantities from the data structures.
  - The log scanner similarly identifies all log statements and constructs appropriate routines to contain this auto-generated log code.
  - Developers can then simply pass in data structures they want to be included in a log and all loggable quantities are automatically extracted and appropriate log definitions generated.
- Languages with reflection and code generation can do this at start-up or using a command line option / special build options during a post-build step to exploit the language features and simplify the implementation.
  - Only usable with some languages (e.g. C#) and if the execution environment allows / done with a special build to circumvent runtime resource restrictions.

---
Log filtering
- The simplest filtering is a general log level setting; each log statement has it’s own severity level determining if it is made.
- A step up is to have a bit array that determines which logs are made.
  - A bit array is fastest for this and scales with the code size so is a reasonable choice for this scenario and as it would usually only be changed by one piece of code there are comparatively few concurrency issues.
- This can be made more complex by temporarily increasing the amount of retained logs in the event of an error which requires:
  - Identifying which log events should trigger this.
  - Which additional logs should be kept (there may not be the bandwidth for all).
  - How to store this O(n2) amount information in a space efficient manner requires an efficient storage method suitable to the data (e.g. a run-length encoded bit array).
  - With a prior log triggering system you always have to temporarily store the additional logs in case they are needed. This is not needed if only subsequent additional logs are to be be made once triggered.

---
Deferred execution
- The key feature of deferred execution is to queue up the generation of a log entry with the data it is to be generated from until later.
  - The actual logging activity can then be performed outside of the main execution path, minimising the impact of the main code latency.
- Gathering together the data to generate the log entry from may not be trivial or fast; any data that might change while the log entry is deferred must be copied.
  - Immutable data objects assist this greatly as a reference such objects can be quickly and simply taken without being concerned about mutability.
- A trade off needs to be performed between:
  - How much data to blanket copy within the logging context.
  - Preparing the log data blob in the logging context.
  - The maintenance of doing so correctly and completely.
  - Flexibility of logging and unobtrusiveness into the source code.

---
Highly concurrent systems
- There will be many contexts attempting to log data and they must be able to do so without stumbling over or blocking each other.
  - The standard solution to this is to have per execution context log queues (no data write contention) and aggregate the logs down, reordering them as appropriate with a single reader of each queue (no data removal contention).
In order to correctly chain logs together into a sequence, use a data ID and processing step count embedded in the data being passed around to be able to reconstruct the sequence of events.
  - The initial step number for an ID is arbitrary but you do need to ensure that it won’t become ambiguous so start new ID step numbers close to large recently used step numbers (e.g. 45698)
Execution context A generating logs
Execution context B generating logs
Log combiner attempts to ensure the logs are ordered appropriately
Freshly arrived
data
ID A
Step: 1
New data arrives to be processed
Preprocessed
data
ID A
Step: 2
Program
state
ID B
Step: 45694
Modified by
program state
ID A
Step: 45695
Postprocessed
data
ID A
Step: 45696
Result leaves
Updated
state
ID B
Step: 45697

---
Log aggregation
- This is the process of incorporating the logs from many running systems into a single server and providing analysis, search and display functionality.
- Of particular interest is the ability to run arbitrary analysis functions over the logs to extract derived quantities and find correlations, e.g.:
  - Compute total instantaneous load on a system and correlate load spikes with particular accounts or data connections.
  - Identify accounts or data connections that cause a higher than normal load.
  - Pattern match state of health telemetry against the conditions before the time of a failure to see if there are any predictive signals and attempt to rule out health measurements that are unlikely to be a predictive cause.
  - Assemble an empirical model of the normal operating conditions and highlight anomalies for investigation or rectification.
- Off the shelf software may not be up to the task of analysing this data; providing an easy to use API for engineers to write their case specific analysis scripts / programs may be more productive.

---
Query mechanisms
- A query is a computation that can be applied to each log entry that both determines if a log entry is in the result set and compute particular values for each result (e.g. a SQL query using stored functions).
  - For logs, a standard database may be significantly outperformed (i.e. be cheaper to run) by a less capable persistence system.
    - Logging based on flat, indexable, binary files or specialist databases can be over an order of magnitude faster at the expense of both functionality and relying on delayed writes.
- For a small log, especially if held in RAM, simply running a selection function over each log entry can be the most efficient.
- For large logs, especially if held on slow non-volatile storage, indexes and pre-computed functions can accelerate the queries at the cost of storage space.
  - Including frequently requested calculation intermediate results (e.g. some calculated system load levels) and derived data computed at the time of log arrival (e.g. system load, time averaged decimation layers and system state visualisation data) should be considered to speed up queries; each log entry gets read many times but only written once.

---
Dynamic logging settings
- Allowing logging to be adjusted at run time allows developers, maintenance and operations staff to investigate issues in production.
  - No need to either re-start production system in ‘debug’ mode or have a torrent of logs being generated as standard.
  - Turn up the logging in areas of interest to investigate behaviour or gather operational behaviour.
  - Avoids having to guess the future at implementation time.
  - Remember to include logging about the overhead cost of logging itself so staff can see the CPU, RAM, disk and bandwidth impact and it van be regulated.
- For deployed systems and clusters, use a centralised logging manager so you can adjust the logging across the entire system centrally.
  - Log settings changes need to be co-operatively managed to both keep the system working normally and co-ordinating the disparate logging requests.
    - Use persistent sessions tied to particular members of staff / teams with separated log requirements to prevent one user clobbering other users.
    - Apply CPU / RAM / disk / bandwidth usage limits to prevent inadvertent performance impacts.

---
Dynamic logging code
- Use an ability to perform arbitrary functions at run-time to allow remote control of the logging code.
  - Maximises the chance that you can collect the data that you need.
  - Can be implemented using log stubs at the start and end of every function (as well as being enabled in all log statements).
  - Also do whole system monitoring on a periodic basis; using immutable data assists in this greatly.
- Languages implementing reflection allow a string name based mechanism for examining state.
  - Requires a domain specific language to specify and a interpreter/executor built into the process; the possible functionality is fixed at compile time.
  - Consumes much more CPU time than hard coded log statements.
- Perform code injection via logging plug-ins.
  - Almost as fast to execute as hard coded logging statements.
  - Maximum flexibility but also no restrictions to void disaster / exploitation.

---
Security implications
- Any kind of access to configure or view logs has security implications.
  - Use your existing IT access and privilege control system rather than re-invent it.
    - Not having a business wide single point of control for granting and removing access to all company systems would be inadvisable.
  - Use encrypted data pipes as standard (preventing unauthorised users from snooping).
  - Encrypt your logs when stored permanently.
    - Data written to disk (even temporarily) can resurface when you least want it to.
    - This is an entire sub-system in and of itself; keys need to be stored and regularly changed in a way that allows access without exposing the keys themselves or locking you out of the logs if you have to restore data from a backup.
  - Always log every log access and settings change against the user who did it.
    - It should never be possible to disable this or erase the data.
    - Implement an automatic behaviour monitor to identify anomalies.
    - Display the current activity and show the anomalies in the office on a flat screen TV so that people can see and act on anything unusual (if only to get themselves off the suspect list).
- Systems that allow arbitrary logging plug-ins have a huge potential for exploitation; consider the pro’s and con’s carefully.

---
Privacy implications
- Including user data in logs has significant regulatory, certification and legal issues; it is generally preferable to avoid logging user data.
  - Many businesses have legal obligations to retain unmodified user data; holding this data separately with it’s own access control is recommended.
  - Have regular data audits to identify and fix violations of your user data policies.
  - Using user identification hashes and assigning short-lived IDs to data with limited meta-data (e.g. data volume) tends to be sufficient for most logging purposes.
  - Ability to select arbitrary data for logging (e.g. a reflection or plug-in system) can easily violate this.
- If the implementation language supports it, annotating user data so it is automatically excluded from logs is helpful.
  - Reflection / plug-in based systems can therefore automatically recognise data fields that are not to be logged.
  - This could be something as simple as implementing an IUserDataAnonomising interface for objects containing user data.