External wired chip access
Pros and cons of some approaches

---
External wired chip access?
- This is an externally accessible data bus that can be used to communicate with your chip on a regular to very rarely basis.
- It is not intended to be used by the primary functioning of the device.
  - You can share an internal data bus externally deliberately but the considerations for doing so is beyond the scope of this presentation.
- Typical usages:
  - Loading firmware.
  - Performing testing.
  - Tracing and getting debug information out.
  - Interactive firmware debugging.
  - Configuring and securing a device.
- Not considering wireless communication (e.g. wifi, bluetooth)
  - Usually much more complex and costly to implement.

---
USB 2 based
- Have a USB connection for external access.
- Requires 2 pins (D+, D-) and can be fast (up to 100’s Mbps) if you have sufficiently powerful microprocessor.
- Allows you to multiplex many chip functions as separately connectable end points.
- Have to license special purpose silicon when designing in-house and have an on-chip USB stack with potential licensing issues (e.g. commercial vs MIT) and has non-trivial processor usage.
- MIT library: https://github.com/hathach/tinyusb
- Non trivial delay needed for enumeration, driver loading and application recognition if boot time access is desired; consider adding an initial boot stage which can be configured to bring up the USB interface and delay the boot to allow enumeration.
- If switching images, the USB stack operation must be undisturbed.

---
JTAG
- Use the JTAG TAP to supply a bidirectional communication link with purpose designed silicon.
    - Well established traditional method that works well with manufacturing test equipment.
- JTAG probes are commonly available.
- 4 pins are needed for full JTAG (TDI, TDO, TCK, TMS + optionally TRST).
- 2 pins are needed for cJTAG (TMSC, TCKC) or SWD (SWDIO, SWCLK).
- Fast (up to ~100 Mbps).
- Have to license special purpose silicon (SWD is much cheaper).
- Generally don’t need any on-chip software beyond enable/disable.
- Operates independently of chip reset / boot, but need to have previously established a connection.

---
Custom firmware managed serial
- Using a serial interface of your choice (SPI, I2C, bidirectional / half-duplex USART) using 1-3 pins and standard serial peripherals.
    - No widespread standard so this is most likely an in-house design.
- USB based generic FTDI adapters are commonly available.
    - Will usually need to make a custom adapter cable unless you have copious board space to put a specific module footprint on your board.
    - Usually easier to just put an FTDI chip using USB directly onto your PCB.
    - You will need to write a PC application to drive the FTDI device and operate your chosen interface and protocol.
- Only need an appropriate peripheral for your chosen signalling.
- Need to have on-chip software support.
    - If you want to implement breakpoints and stepping then you’ll either need H/W breakpoints or the ability to modify the executing code.
    - Requires mostly bespoke software.
- Typically sluggish (~1Mbps) unless implemented efficiently (~10Mbps).

---
Custom debugging firmware
- Needed for on-chip USB or custom firmware managed serial.
- The firmware needs to operate all debugging operations.
- There is a significant amount of processor load on the chip as a result which limits the effective speed of operations (rather than the communication speed).
- General architecture:
- This is usually a software capability built up over years.
USB or
serial
Command &
data buffers
PC utilities
with GDB portal
Peripheral ISR
+
Protocol stack
ISR debug agent
Task debug agent
In code debug agent
H/W address ISR
RAM contents
Exec binary
Debug info
Peripherals
Task & ISR priorities

---
Breakpoints and code stepping
- Code stepping is simply putting breakpoint(s) in appropriate places so that only one line of code is executed before hitting the next breakpoint.
- H/W breakpoints are actually a hardware address matching feature.
  - The next instruction address (program counter) is compared against a fixed number (usually 2-6) of addresses.
  - For custom debug firmware to be able to use this an interrupt must be raised (rather than halting the processor and passing control to a H/W debugger).
  - The debugging agent then takes control and informs the GDB clients of the new processor state.
- Code modification breakpoints rely on changing the code so that the in task / in ISR debug agent is called.
- If code modification is not possible then a large number of ‘should I break now’ checks can be inserted by build tools in areas of interest.
  - The developer can only break at these particular locations.